Counter specification

Company : Elsys Eastern Europe
Author : Andrea Erdeljan
E-Mail : andrea.erdeljan@elsys-eastern.com
Mentor : Darko Tomusilovic
Revision History
Rev.	Date	Description
0.1	14.9.2015.	Initial

# 1. Introduction

This counter design is Verilog RTL model which implements a 16-bit up/down counter with AXI4 full protocol support and interrupt signals.
## Highlights
- 16-bit up/down counter
- AXI4 protocol compliant
- contains RIS, IM and MIS registers
- LOAD register
- counter enable, direction
- MATCH register
- IIR register
- reset counter on edge, SWRESET
- two clock domains
# 2. Interface
The counter interface is described in this section.
## 2.1 Parameters
Name	Type	Description
ID_WIDTH	Integer	Width of ID for for write address, write data, read address and read data
DATA_WIDTH	Integer	Width of AXI data bus
ADDR_WIDTH	Integer	Width of AXI address bus
AWUSER_WIDTH	Integer	Width of optional user defined signal in write address channel
ARUSER_WIDTH	Integer	Width of optional user defined signal in read address channel
WUSER_WIDTH	Integer	Width of optional user defined signal in write data channel
RUSER_WIDTH	Integer	Width of optional user defined signal in read data channel
BUSER_WIDTH	Integer	Width of optional user defined signal in write response channel

## 2.2 Signals
Name	Width	In/Out	Description
Full AXI4
FCLK	1	Input	Counter clock
IRQ_O	1	Output	Interrupt
DOUT_O	1	Output	Is counter > LOAD
RESET_I	1	Input	Resets counter on rising edge

# 3. Internal Registers
Name	Width	Description		Address
RIS	[DATA_WIDTH-1 : 0]	Register interrupt status, set by hardware when an interrupt occurs / bit 0 – overflow / bit 1 – underflow / bit 2 – match	Read-only	0
IM	[DATA_WIDTH-1 : 0]	Interrupt enable / bit 0 – overflow / bit 1 – underflow / bit 2 – match	Read-write	2
MIS	[DATA_WIDTH-1 : 0]	Masked intrrupt status / bit 0 – overflow / bit 1 – underflow / bit 2 – match / additional functionality: writing 1 to a correct bit location clears the flag in RIS and MIS registers, but only if PROT = 1 (writing 0 does nothing, when PROT = 0 nothing)	Read_write	4
LOAD	[DATA_WIDTH-1 : 0]	Counter is being compared to this value and DOUT_O set accordingly	Read-write	6
CFG	[DATA_WIDTH-1 : 0]	Configuration register / bit 0 – counter enable / bit 1 – up (0) or down (1)	Read-write	8
SWRESET	[DATA_WIDTH-1 : 0]	Writing the code (0x5a) resets all registers / other writes do nothing / read always returns 0	Read-write	10
IIR	[DATA_WIDTH-1 : 0]	Interrupt index register – priority register / MIS[2:0]=1xx – value = 3 / MIS[2:0]=01x – value = 2 / MIS[2:0]=001 – value = 1 / reading it clears the highest priority interrupt	Read-only	12
MATCH	[DATA_WIDTH-1 : 0]	Counter is being compared to this value. When equal to it the match interrupt occurs and RIS[2] is set	Read-write	14
count_aclk	[DATA_WIDTH-1 : 0]	Value of the counter	Read-only	16

*note: all unimplemented bits are read-only, value = 0
# 4. Clock domains
Two clock domains are used for this design:
1. AXI_ACLK – controls all the registers and the AXI interface
2. FCLK – controls the counter

Crossing clock domains is done using synchronizers, as follows:
- Overflow or underflow in the counter sent to RIS[0] or RIS[1] via the edge detector
- Match interrupt in the counter is sent to RIS[2] via the edge detector
- changes in the CFG register are sent to the counter via a simple 2 flip-flop synchronizer
- nrst signal (based on SWRESET register) is sent to the counter via the edge detector
- RESET_I (input reset on edge) is sent to the counter via the edge detector
- the dout_o value is set via a simple 2 flip-flop synchronizer
- count value from counter is sent to the count_aclk register and LOAD and MATCH values to the counter using a two-phase handshaking protocol (counter sets the req and put the data on the data_bus, when the req is sensed the data is collected, ack is raised and the LOAD and MATCH values placed on the bus (from the AXI_ACLK domain); when the counter senses the ack signal it can start a new transaction by lowering the req and when the data is collected the ack is lowered; when the counter senses the low ack it can initiate a new transaction, and so on...)
# 5. AXI4 transactions
AXI read and write burst requests should be as follows:
- DATA_WIDTH should be 16
- valid AxADDR values are 0, 2, 4, 6, 8, 10, 12, 14 or 16
- value of AxLEN should be 0 (burst length = 1 transfer)
- size should match the DATA_WIDTH (AxSIZE = 1 (16 bits))
- burst type should be FIXED (AxBURST = 2'b00)
- AxID should be 0
- all other signals can have any value
Any deviation from these specified values will result in the counter returning a SLVERR